## Slide 1
CAPSTONE MAJOR PROJECT — PHASE-I APPROVAL
Battery Management System
& Hybrid Bridge Digital Twin
Under the Guidance of Dr. Avinash More & Dr. Anjana Rodrigues
Krish Rajgor
D023 — 70062300033
Harshwardhan Patil
D048 — 70062200035
Nihar Lad
D038 — 70062100151
B.Tech Electronics & Telecommunication Engineering
SVKM's NMIMS — MPSTME, Mumbai | Academic Year 2024–25 / 2026–27 | Semester VII
SVKM's NMIMS | MPSTME | Dept. of E&TC
1

## Slide 2
MOTIVATION & INTRODUCTION
Why a Smart BMS Is Necessary
Li-ion batteries operate in a narrow safe window. A BMS monitors, protects and manages the pack. The weakest cell limits the entire series pack — not total pack voltage.
OVER-CHARGE
Cell voltage exceeds safe limit — degradation risk
DEEP DISCHARGE
Cell voltage too low — capacity loss & damage
CELL IMBALANCE
Cells drift to different voltages — capacity lost
THERMAL RISK
Temperature beyond limit — fast protection needed
CELL 1
4.18 V
CELL 2
4.12 V
CELL 3
4.20 V
CELL 4
4.05 V
SVKM's NMIMS | MPSTME | Dept. of E&TC
2
Notes: Presenter 1 — Krish. Cover motivation + cell-level monitoring importance.

## Slide 3
PROBLEM & OBJECTIVES
Engineering Challenge & Goals
CURRENT STATE
Cells differ in capacity, resistance & thermal behaviour
Mismatch causes uneven charge/discharge
Commercial solutions costly for prototypes
DESIRED SOLUTION
Modular embedded BMS for real-time monitoring
Pack protection during abnormal conditions
Cell balancing + SOC + wireless diagnostics
PROJECT OBJECTIVES
01
Cell Voltage Monitoring
02
Current & Temperature Sensing
03
Passive Shunt Balancing
04
SOC via Coulomb Counting
05
OVP/UVP/OCP/OTP Protection
06
OLED + Wi-Fi Diagnostics
SVKM's NMIMS | MPSTME | Dept. of E&TC
3
Notes: Presenter 1 — Krish. Problem statement + six objectives.

## Slide 4
RELATED WORK
Literature Survey & Gap Analysis
Focus Area | Approach | Strength | Limitation
SOC Estimation | EKF / model-based | High accuracy | Computationally complex
Cell Balancing | Passive resistor shunt | Simple & low-cost | Energy lost as heat
Thermal Monitoring | Multi-point NTC | Low-cost coverage | Limited remote visibility
Fault Protection | Solid-state switching | Fast response | Higher complexity
PROJECT GAP: A modular platform combining cell-level sensing, passive balancing, SOC estimation, fault protection, and OLED/Wi-Fi diagnostics at embedded-system level.
SVKM's NMIMS | MPSTME | Dept. of E&TC
4
Notes: Presenter 1 — Krish. Literature table + gap.

## Slide 5
ARCHITECTURE & HARDWARE
System Design & Components
3S/4S
BATTERY
CELL V
SENSING
I + T
SENSING
STM32
CONTROL
SOC
ESTIM.
BALANCE
+ PROTECT
OLED
Wi-Fi
Sensing → Processing → Decision → Action
Component | Function | Specification
STM32 | Control, ADC, Wi-Fi/BT | 32-bit dual-core, 12-bit SAR ADC
ACS712 | Bidirectional current | Hall-effect sensor
10k NTC | Temperature monitoring | Voltage-divider arrangement
MOSFET+Shunt | Passive balancing | Controlled dissipation path
Optocoupler | Stage isolation | Control/power isolation
OLED/Wi-Fi | Diagnostics | Real-time status & alerts
SVKM's NMIMS | MPSTME | Dept. of E&TC
5
Notes: Presenter 1 — Krish. Architecture block diagram + component table.

## Slide 6
METHODOLOGY
SOC Estimation, Balancing & Protection
1
SENSE
V, I, T
→
2
PROCESS
Validate
→
3
INTEGRATE
Coulomb Count
→
4
CORRECT
V correction
→
5
REPORT
OLED+Wi-Fi
SOC(k) = SOC(k−1) − [ I(k) × Δt / Capacity ] × 100
PASSIVE BALANCING
HIGH-V
CELL
→
MOSFET
SWITCH
→
10Ω SHUNT
→
HEAT
DISSIPATED
PROTECTION LOGIC
Type | Trigger | Action
OVP | V ≥ 4.25V | Open charge
UVP | V ≤ 2.80V | Isolate load
OCP | I ≥ 15A | Shutdown
OTP | T ≥ 60°C | Isolate pack
Balancing: simple & low-cost | Limitation: energy dissipated as heat
SVKM's NMIMS | MPSTME | Dept. of E&TC
6
Notes: Presenter 2 — Harshwardhan. SOC pipeline + formula + balancing flow + protection table.

## Slide 7
FIRMWARE & VALIDATION
Control Loop & Testing Plan
START
Init Sensors
Read V, I, T
SOC + Faults
FAULT → Alert
Balance
OLED + Wi-Fi
Layered: Sense → Process → Estimate → Protect → Actuate → Report
VALIDATION PLAN
✓ Cell voltage ✓ Current sensing ✓ Temperature ✓ Balancing
✓ OVP/UVP ✓ OCP/OTP ✓ SOC estimation ✓ Wi-Fi monitoring
COST BREAKDOWN
Battery 24% | STM32 18% | Sensors 18%
MOSFET 16% | Display 14% | Misc 10%
SVKM's NMIMS | MPSTME | Dept. of E&TC
7
Notes: Presenter 2 — Harshwardhan. Firmware loop + validation checklist + cost.

## Slide 8
PROJECT TIMELINE
Semester Gantt Chart
W1
W2
W3
W4
W5
W6
W7
W8
W9
W10
W11
W12
W13
W14
W15
Lit Review & Topic
System Design
Review 1
Circuit & Firmware (BMS)
Bridge & Sensors (DT)
Review 2: Midterm
Integration & Testing
Dashboard & Model (DT)
Documentation
Review 3: Final
SVKM's NMIMS | MPSTME | Dept. of E&TC
8
Notes: Presenter 2 — Harshwardhan. Walk through the 15-week Gantt chart with review milestones.

## Slide 9
BMS SCOPE
Applications, Limitations & Future
APPLICATIONS
2W/3W electric mobility
Solar PV energy storage
Stationary BESS
Robotics and UAVs
Educational platforms
LIMITATIONS
Passive balancing dissipates energy
Coulomb Counting drifts
Low-cost sensor accuracy limits
Limited thermal management
Scalability needs further work
FUTURE SCOPE
Active balancing
CAN Bus integration
EKF/UKF SOC estimation
SOH + ML prediction
Cloud monitoring + thermal
SVKM's NMIMS | MPSTME | Dept. of E&TC
9
Notes: Presenter 2 — Harshwardhan. Applications, limitations, future scope.

## Slide 10
PRESENTER 3 — PROJECT 2
Hybrid Bridge Digital Twin
Real-Time Structural Health Monitoring
1. Civil infrastructure faces continuous environmental stressors and dynamic traffic loads
2. Traditional visual inspections lack real-time awareness — Digital Twins synchronize physical assets with computational models
3. Our project: functional DT using affordable IoT sensors and RGB-D depth mapping
4. Motivation: DT adoption bottlenecked by prohibitive LiDAR & proprietary DAQ costs
SVKM's NMIMS | MPSTME | Dept. of E&TC
10

## Slide 11
PROBLEM, LITERATURE & OBJECTIVES
The Industry Gap & Project Goals
No integrated, low-cost framework merges multi-parameter sensing, depth-camera baselining, and predictive FE modeling for real-time structural anomaly detection.
Wireless SHM
ESP32/Pi log data but lack model comparison
Vibration Detection
Frequency shifts flag stiffness loss; needs thermal compensation
RGB-D Baselining
Low-cost RealSense viable for 3D geometry vs LiDAR
OBJECTIVES
01
Fabricate 3D-printed truss bridge testbed
02
Integrate multi-sensor suite (strain, vibration, load, temp)
03
Implement depth camera for 3D baseline geometry
04
Develop Reduced-Order Finite Element Model (ROM)
05
Classify health: Normal / Warning / Damaged
SVKM's NMIMS | MPSTME | Dept. of E&TC
11
Notes: Presenter 3 — Nihar. DT problem + literature cards + objectives.

## Slide 12
ARCHITECTURE & COMPONENTS
System Layers & Tech Stack
PHYSICAL LAYER
3D-printed truss bridge on mechanically controlled loading rig
SENSING LAYER
Strain gauges, 3-axis accelerometer, load cell (HX711), DHT22, Intel RealSense D435
COMPUTATIONAL LAYER
Python Reduced-Order FE Model + FastAPI/WebSocket + React/Plotly dashboard
HARDWARE
Intel RealSense D435 RGB-D Camera
Strain Gauges & 3-Axis Accelerometer
Load Cell (HX711) + DHT22 Temp
STM32 Microcontroller Edge Node
SOFTWARE
Backend: Python, FastAPI, WebSockets
Analysis: FFT scripts for vibration
Modeling: Reduced-Order FE Model
Frontend: React & Plotly Dashboard
SVKM's NMIMS | MPSTME | Dept. of E&TC
12
Notes: Presenter 3 — Nihar. Three architecture layers + HW/SW stacks.

## Slide 13
METHODOLOGY & APPLICATIONS
Phased Approach & Use Cases
Phase 1–2
Fabrication, sensor mounting & baseline 3D scanning
Phase 3
Static loading & dynamic vibration tap testing (FFT)
Phase 4–5
Model calibration & live dashboard anomaly validation
Phase 6
System optimization, latency testing & documentation
KEY APPLICATIONS
Municipal Infrastructure
Cost-effective bridge monitoring
Disaster Response
Rapid post-earthquake assessment
Smart Cities
Cloud-connected predictive maintenance
Industrial
Conveyor truss & gantry health monitoring
Key References
[1] Farrar & Worden (2012) — SHM [2] Tao et al. (2018) — DT in Industry [3] Torzoni et al. (2020) — SHM via ROM [4] Ye et al. (2016) — Structural Displacement
SVKM's NMIMS | MPSTME | Dept. of E&TC
13
Notes: Presenter 3 — Nihar. DT methodology phases + applications + references.

## Slide 14
ACKNOWLEDGEMENT
With Gratitude
We express our sincere gratitude to our guides, Dr. Avinash More and Dr. Anjana Rodrigues, for their invaluable mentorship, guidance and support throughout this project.
Special thanks to the Department of Electronics and Telecommunication Engineering at MPSTME, SVKM's NMIMS, for providing the necessary laboratory facilities and resources.
Krish Rajgor
Roll No: D023
Harshwardhan Patil
Roll No: D048
Nihar Lad
Roll No: D038
SVKM's NMIMS | MPSTME | Dept. of E&TC
14
Notes: Presenter 3 — Nihar. Acknowledgement.

## Slide 15
CONCLUSION
From Monitoring to Intelligence
Battery Management System
✓ Cell-level V, I, T monitoring
✓ ESP32 real-time control
✓ Passive balancing + Coulomb SOC
✓ Multi-level OVP/UVP/OCP/OTP
✓ Modular platform for future work
Hybrid Bridge Digital Twin
✓ Low-cost RGB-D + IoT framework
✓ 3D-printed testbed + multi-sensor
✓ Reduced-Order FE Model
✓ Real-time health classification
✓ Scalable to municipal & industrial
Both projects demonstrate how embedded systems, sensing, and computational models
can improve safety, reliability and observability in critical applications.
Thank You | Questions & Feedback